## Slide 1
Anastasios Karles, David Brimmer, Yaritna Matos-Ramos, Michael Baedke
Human-Centric Approach to Design of Sixthman User-Interface and User-Experience

## Slide 2: Introduction
Advances in grid-monitoring technologies allow us to better understand unfamiliar dynamic behaviors and navigate the complex operations and controls required to maintain grid reliability [1].
Challenges persist in navigating the “ocean of information” [2] that arises from the proliferating data [1][3].
Substation A
Substation B
Substation C
Substation D
Notes: Without effective visualizations and human-centric frameworks for the design of SA tools, the data becomes overwhelming, rather than advantageous.

## Slide 3: Human Errors & Decisions
Human errors are largely linked to cognition.
In simulated experiments that employed the use of a digital control system in operating a nuclear power plant, most errors were due to distracted attention or mistaken intention when executing a task [4].
Decision making is a complex cognitive activity, hierarchal in nature, and affected by external representations
Events
Actions
Tasks
Cognitive Activities
Notes: Whether for grid management or fault analysis, human-centric design necessitates an understanding of the cognitive components that influence performance, especially for systems that pertain to decision-making or situational awareness.
Decision making is a complex cognitive activity, hierarchal in nature, and affected by external representations; low-level events generate higher-level actions, which generate the higher-level tasks from which cognitive activities emerge [5].

## Slide 4: Cognitive Load
Cognitive load is analogous to power system load and concerns the consumption of cognitive resources.
Intrinsic
Germane
Unnecessary information or stimuli that impede information processing.
Integrating new information with a priori knowledge.
Inherent complexity of processing information.
Extraneous
Notes: Precise tasks inherently involve high mental workload, which is exacerbated by the need to process more information within a shorter timeframe.
While power systems are subject to residential, commercial, or industrial load, our cognition is subject to various types of intrinsic, extraneous, and germane load [9][10].
Mitigating factors of extraneous cognitive load frees mental resources that would otherwise inhibit our already limited information processing capabilities [7][8][11]. Designing systems with cognition in mind enhances human-computer interaction and performance [12].

## Slide 5: Cognitive Task Analysis (CTA)
CTA “focuses on how humans receive and process information in performing a task and how the task can be enhanced to improve human performance” [5].
The primary step of any task analysis is knowledge acquisition about the tasks and sub-tasks related to the system under design [5].
  Techniques of knowledge acquisition that were employed in our knowledge acquisition step include questionnaires, informal interviews, and naturalistic observation.
Notes: To understand the cognitive components that influence performance during real-time fault analysis, we perform a Cognitive Task Analysis (CTA).
Coupling our CTA with a traditional task analysis that involves decomposing the actions, tasks, and decisions a user must make into an atomic form allows us to model our users’ decisions. These models facilitate the adaptation of the user-interface and automation to the context-specific cognitive and task requirements of our users.

## Slide 6: Sixthman Case Study
CTA was conducted with six members of Dominion’s System Protection Automation and Analysis (SPAA) team who perform real-time fault analysis on a duty rotation.
25 Question Survey
Task Sequences
Error Handling
Mental State
Usability
Stereotype Processes
Areas for Automation
Cognitive Loads
Guidance Features
Long-Term Historical Analysis
Notes: CTA was conducted on six members of Dominion’s System Protection Automation and Analysis (SPAA) team who perform real-time fault analysis on a duty rotation.
The members, with experience levels ranging from <1 year to >10 years, answered a 25-question survey categorized into four main question types: tasks, error handling, mental state, and usability. Naturalistic observation was conducted during working hours and bi-weekly fault analysis meetings, where the team discusses unique events and potentially unfamiliar scenarios that may be encountered during real-time analysis. These knowledge acquisition procedures allowed us to identify factors that contribute to extraneous cognitive load and model the action sequences and stereotype process used in real-time decision making.

## Slide 7: Evaluating Tasks
Task-units were combined into a network of representative questions, where the edges represent some ontological relationship between the nodes.
Check Operation Quick Summary
Missing Data:
Check Fault Location Summary Tables
Receive Notification from SOC.
Check Automated Sixthman Report.
Verify Estimated Locations Using Manual Methods.
Confirm Location/Structure with Field.
Check Historical Location Data
Notes: By asking participants to present their tasks in terms of hierarchal action-sequences involved in the activity, we identified individualistic task-units used in real-time analysis. These task-units were used to develop an atomic decision tree that encompasses most “paths” that can be used to come to a decision. Visual observation was used to identify action-sequences that can be automated or aided by changes to the user-interface or user-interaction.
Diagnosing the “missing data state” is not navigating a labyrinth; however, it is a superfluous web, especially when the entire collection of “Missing Data’ nodes could be removed from the decision sequence with automation. Automating such a simple problem may seem inessential; however, it is still one way to potentially prevent undesirable cognitive states and human error.

## Slide 8: Evaluating Mental State
Participants were questioned on the likelihood of experiencing undesirable mental states.
Note the increase in likelihood of perseveration, defined as the tendency to persist with erroneous strategy when generally capable of performing the required tasks [6].
Emergency
Standard
Notes: The answers to these questions were used to characterize the influence that cognitive load might have on performance and identify the factors that required mitigating procedures. Other than effort withdrawal, all states were rated to be more likely to occur during an emergency scenario, where individuals might have to analyze concurrent events at the same time. Of note is the increase in likelihood of perseveration, which is defined as the tendency to persist with erroneous strategy when generally capable of performing the required tasks [9].

## Slide 9: Evaluating Usability & Guidance
Participants were also questioned on their communication practices and how they self-monitor their progress towards their analysis goal.
Other lines of questioning involved:
  Communication practices.
    They noted a strong desire for standardized responses and the ability to reference past communication, despite the availability of historical post-mortem analysis.
  Self-monitoring of progress towards analysis goal.
    Identified as a factor of extraneous cognitive load.
  Level of information overload.
    The desire to control the visibility of certain data through filtering is prevalent and in-line with usability principles.
  Level of multitasking.
  Level of desired guidance.
Notes: The lack of a standardized response form was identified as a contributor to cognitive load. A standardized response form would mitigate the extraneous cognitive load caused by the self-monitoring of task completion. Guidance interaction can be added to the form to mitigate potential perseveration behaviors.

## Slide 10: Evaluating Heuristics
Participants’ rankings of their confidence in calculation methods compared to the median error of each method calculated for a set of operations that occurred as far back as 2012.
Notes: Confidence Rankings

## Slide 11: Line Profiles
Notes: Historical fault location estimates were analyzed to create “fault estimation profiles” categorized by line and fault incident
These profiles provide a visual method to keep track of the accuracy of different calculation methods for each line and can be further categorized by fault type, fault cause, or other parameters. Despite the high potential for variance in the estimated fault location, most operations have at least one fault-location estimate within three to five structures of the reported structure. Note that these are only the estimates provided by different calculation methods and do not represent the actual structure shared with the field.

## Slide 12
Notes: Historical Analysis

## Slide 13
Notes: Historical Analysis

## Slide 14
Notes: Historical Analysis

## Slide 15: Lessons Learned (CTA)
Open-ended questions should be very specific and have a narrative.
Questionnaires always take longer than designed.
Atomized decision sequences are nearly impossible to effectively visualize.
Notes: Specific questions require a priori information. It would have been better to treat it as if a text adventure game was being designed.
Image source: https://miro.medium.com/max/2690/1*RSPFY1KviyRLQeA2ZKmtPw.png

## Slide 16: Discussion & Future Work
Prototype user-interfaces and user-interactions based on CTA results.
Perform CTA with secondary and tertiary users using lessons learned.
Create standardized form-based communication and response procedures.
Extend line profiles to other categories (e.g. fault type & distance from terminal).

## Slide 17: Questions?

## Slide 18: References
[1] M. Pertl, M. M. N. Rezkalla, and M. Marinelli, "A Novel Grid-Wide Transient Stability Assessment and Visualization Method for Increasing Situation Awareness of Control Room Operators," 2016 IEEE PES Innovative Smart Grid Technologies Asia (ISGT-Asia), Melbourne, VIC, Australia, 2016, pp. 87-92, doi: 10.1109/ISGT-Asia.2016.7796366.
[2] G. Abowd, G. Hayes, G. Iachello, J. Kientz, S. Patel, M. Stevens, and K. Truong, "Prototypes and Paratypes: Designing Mobile and Ubiquitous Computing Applications," IEEE Pervasive Computing, vol. 4, no. 4, pp. 67-73, Oct.-Dec. 2005.
[3] A. Marot, A. Kelly, M. Naglic, V. Barbesant, J. Cremer, A. Stefanov, and J. Viebahn, "Perspectives on Future Power System Control Centers for Energy Transition," Journal of Modern Power Systems and Clean Energy, vol. 10, no. 2, pp. 328-344, Mar. 2022, doi: 10.35833/MPCE.2021.000673.
[4] Jiajun, Y. (2017). Study on Human Errors in DCS of Nuclear Power Plant. In: Jiang, H. (eds) Proceedings of the 20th Pacific Basin Nuclear Conference. PBNC 2016. Springer, Singapore https://doi.org/10.1007/978-981-10-2311-8_58
[5] C. M. Harvey, L. Rothrock, and J. W. Kim, "Cognitive Ergonomics," in Handbook of Human Factors in Web Design, 2nd ed., K.-P. L. Vu and R. W. Proctor, Eds. Boca Raton, FL, USA: CRC Press, 2011, pp. 123-145.
[6] F. Dehais, A. Lafont, R. Roy, and S. Fairclough, "A Neuroergonomic Approach to Mental Workload, Engagement and Human Performance," Frontiers in Neuroscience, vol. 14, pp. 268, Mar. 2020, doi: 10.3389/fnins.2020.00268.